## Slide 1: Constructing seamless MODIS LST maps for Australia from swath data C. Bossung; K. Mallick; M. Schlerf
CCI LST User Workshop
24-26 June 2020

## Slide 2: Original user case idea
Integration of CCI+ LST in a SEB model for simultaneous estimation of evaporation, transpiration and water stress, and validation across an aridity gradient and multiple biomes.
Evaluation of SEB model in the context of multi-sensor CCI+ LST data uncertainty and spatio-temporal stability.
Comparing multi-sensor CCI+ LST with Insitu LST
Source: Rogers, C. & Beringer, J. (2017), Biogeosciences, 14, 597-615, 10.5194/bg-14-597-2017.

## Slide 3: Outline
Project overview
Challenges for the creation of the daily mosaics
Processing-Step 1: Re-ordering/structuring the data files
Processing-Step 2: Generating of daily pan-Australian mosaics
Pan – Australian mosaics: first impressions
Conclusions

## Slide 4: Challenges: creation of daily pan – Australian mosaics
File structure on server: for each day all datasets in one folder
Separation btw. MODIS - Aqua / Terra; btw. MODIS and others (ATSR and Sentinel-3 SLSTR)
Distinguish btw. day and night observation; calculating overpass times in UTC
Unclear geo-location in the filename
Strategy: Mosaic all images of each sensor to a respective daily day- and night-time pan-Australian LST mosaic to extract the test sites.
At the end 4 pan-Australian mosaics for each day

## Slide 5: Processing-step 1.1: Re-ordering /structuring the data
Example of the file structure:
For each day all files are in one folder
Filenames does not indicate the geolocation to search directly for the sampling sites.

## Slide 6: Processing-step 1.2: Sensor separation
Data transfer
Data downloaded for each day; consisting of MODIS – A / T and ATSR and SLSTRA (first 2016-10-29)
Filenames consisting name of satellite, platform, date and time (UTC)
Sensor
Date
Time

## Slide 7: Processing-step 1.2: Sensor separation
Sorting/structuring
Structure needed: Sorting for each sensor and day / night observation
Sensor separation relatively easy with splitting the filename and moving the file into a separate folder
Sensor
Date
Time

## Slide 8: Processing-step 1.3: Calculating overpass in UTC; Day-night separation
Main problem: day / night separation; Filenames contain start time of the granule in UTC
Filenames in UTC, time in Australia:
  UTC : xhours, MODIS equatorial crossing time: Terra: 10:30, Aqua: 13:30 (local time)
  Australia time range:
    Terra (Day): 23:30 – 02:30 UTC
    Aqua (Day): 02:30 – 05:30 UTC
    Terra (Night): 11:30 – 14:30 UTC
    Aqua (Night): 14:30 – 17:30 UTC
Strategy: Calculate the potential overpass time for day / night observations in Australia in UTC time and search for this time range in the filenames
Source: https://en.wikipedia.org/wiki/Time_in_Australia#/media/File:Australia-states-timezones.png

## Slide 9: Processing-step 1.3: Calculating overpass in UTC; Day-night separation
Calculate Australian local time range:
Search for the files MODIS A / T in the day time-range and night time-range within the filenames (UTC)
Notes: UTC + 8 hours W to UTC + 10/11 hours E; Matlab function: getOverpassTime2.m

## Slide 10: Processing-step 2: generating daily pan-Australian mosaics
All files (MODIS A/T) have the same geographic extent.
Each day consists of four observations MODIS-Aqua / Terra and day / night
Method: Replace NaN values of the first LST file with LST values of the other datasets in the respective folder (Aqua day / night; Terra day / night)
- With each iteration the search for NaN values is updated
Notes: Easier to extract the test sides, as we were not able to figure out the extent of each raw file.

## Slide 11: Examples: MODIS Terra LST
Day
Night
Jan 07, 2016
Apr 04, 2016
Jul 10, 2016
Oct 04, 2016

## Slide 12: Examples: MODIS Aqua LST
Day
Night
Jan 07, 2016
Apr 04, 2016
Jul 10, 2016
Oct 04, 2016

## Slide 13: Conclusions and Follow up work
Seamless mosaics of MODIS Terra and Aqua day and night LST for Australia were produced for the period of 1 Jan 2001 – 31 Dec 2016.
The mosaics
Serve as input to further SEB modelling and stress index calculations
Allow to analyze LST and ET patterns along aridity gradients
Post lockdown:
Subsetting at least two sites in the north and the south Australia; Insert LST data into a non-parametric surface energy balance model