## Slide 1: Use of LST data for producing data for the FAO-WaPOR portal: past, present and future
Dec 6th 2024
Henk Pelgrum, Joost Brombacher, Karlis Zalite, Steven Wonink

## Slide 2: FAO - WaPOR
WaPOR
  Near real time global database using satellite data that allows the monitoring of agricultural water productivity at different scales
  Capacity building in the use of WaPOR data for different applications
  Generate solutions to local challenges linked to water productivity and land productivity as well as water management
  Training is done by IHE Delft
  Capacity building is done by IWMI
  Data provision (v3.0) is ensured by eLEAF
  Data provisions for previous versions was done by eLEAF and VITO

## Slide 3: FAO-WaPOR requirements
Data used for producing database data should be open source
Software used for producing database is also open source
  PyWAPOR (https://bitbucket.org/cioapps/pywapor/src/master/)
General idea is that users should be able to calculate their own data without additional costs for data
Currently we are on v3 of the dataset

## Slide 4: FAO-WaPOR database content
Evapotranspiration (separated into E, T)
Interception
Land Cover Classification (not in v3)
Net Primary Productivity
Phenology (not in v3)
Precipitation
Quality layers
Relative soil moisture content for the rootzone
Total biomass production
Water productivity

## Slide 5: FAO-WaPOR Coverage
Database version | Description | V1 | V2 | v3
L1 L2 L3 | Continental level Basin level Irrigation scheme | 250 m 100 m 30 m | 250 m 100 m 30 m | 300 m 100 m 20 m
Database version | Description | V1 | V2 | v3
L1 L2 L3 | Continental level Basin level Irrigation scheme | Africa Middle East Major watersheds Africa 10+ areas | Africa Middle East Major watersheds Africa 20+ areas | Global Africa Middle East Pakistan Colombia 30+ areas

## Slide 6: Models
Models used for the main components:
Evapotranspiration & Interception --> ETLook
  NDVI
  Surface Albedo
  Soil Moisture
  Meteorological data
Net Primary Production --> C-fix
  NDVI
  Meteorological data
Soil moisture --> Pixel-based trapezoid approach
  Land Surface Temperature
  NDVI
  Meteorological data

## Slide 7: Data providers
Input Variable | v1 | V2 | v3
NDVI | MODIS Landsat | MODIS Landsat Sentinel-2 | MODIS VIIRS Landsat Sentinel-2
Surface Albedo | MODIS Landsat | MODIS Landsat Sentinel-2 | VIIRS Landsat Sentinel-2
LST | MODIS Landsat | MODIS Landsat | VIIRS Landsat
Meteorological data | MERRA GEOS-5 | MERRA GEOS-5 | (ag)ERA5 GEOS-5

## Slide 8: ETLook
Separate Penman-Monteith for soil and canopy
Computes daily Interception, Evaporation and Transpiration
Reduction of Potential ET through a soil moisture stress factor

## Slide 9: C-Fix model
Radiation based
fPAR is a function of NDVI
Uses similar soil moisture stress as ETLook for reducing NPP

## Slide 10: Soil moisture model
Trapezoid approach
Pixel based instead of image-based

## Slide 11: Soil Moisture: WaPOR vs SMAP
A rudimentary comparison

## Slide 12: Changes in versions related to inputs
MODIS Tile data (v0-v2) -> VIIRS Swath data (v3)
  MODIS/VIIRS Tiles are troublesome when going global!
  Sinusoidal projection
  Instead of using LST as a product, LST is derived from the brightness temperature
For the 100m products (Africa/Middle East/Pakistan/Colombia)
  Resampling -> Thermal sharpening
  Resampling lead to errors on dry/wet boundaries

## Slide 13: Coarse resolution LST products
MODIS
Sentinel-3
VIIRS
GCOM
(not very suitable for operational application)
Euphrates Tigris
 | Spatial resolution (m) | Archive since
MODIS | 1000 | 2000
S-3 | 1000 | 2016
VIIRS | 375 | 2011
GCOM-C | 250 | 2018

## Slide 14: Thermal Sharpening
PyDMS
https://github.com/radosuav/pyDMS
PyDMS application
Feature selection and data preparation

## Slide 15: Thermal sharpening example
VIIRS Brightness Temperature
November 16th, 2024
South-Africa
SEntinel-2 Tile ID: 34HCH

## Slide 16: Water Balance Closure
Water Balance Equation:
Precipitation (P) = Evaporation (E) + Transpiration (T) + Interception (I) + Discharge (Q)
Assessment for four African catchments
On average -1.8% difference between P and sum of E, T, I and Q
Meaning: ETLook is capable of accurately estimating the ETI at catchment level, the model has no systematic bias that results in an unclosed water balance. The individual accuracy of E, T, and I is still unknown.

## Slide 17: Validation
Validation with EC-data in the USA​
Daily data​
Good consistency between L1 and L3 in general

## Slide 18: Validation – L1 vs L3
Spring​
Summer

## Slide 19: Future outlook
New high resolution sensors on the horizon (open data)
Observations instead of artificial sharpened data for L2 and L3
Sensor | Resolution | Revisit time | Launch date
SGB-TIR TRISHNA LSTM | 60 m 60 m 50 m | 3 days 3 days 4 days | 2029 2026 2028 - 2030

## Slide 20
LST is integral part of the WaPOR data pipeline
In the past resampled LST caused issues
Currently thermal sharpening is used to provide high resolution LST
Future versions will incorporate next generation high resolution LST open-source data
Contact:
henk.pelgrum@eleaf.com
Wapor Database:
https://data.apps.fao.org/wapor/