## Slide 1: LST from IR instruments on Polar Orbiting Satellites
Karen Veal, Darren Ghent, and Mike Perry
University of Leicester, NCEO
Notes: Good Morning
I’m Karen Veal from the Surface Temperature Group at University of Leicester. I shall be talking about work done by Darren Ghent, Mike Perry and myself.

## Slide 2: Outline
Approach
Products
  Single sensor products
  Infra-red (IR) Climate Data Record from polar satellite sensors (IRCDR)
  Merged GEO and LEO IR product (IRMGP)
Future developments
Notes: In outline, I’ll start by talking about elements of the approach to developing LST products from the infra-red sensors on polar orbiters in LST CCI.
Note, I will refer to polar orbiters in this talk as LEOs or Low Earth Orbiters.
I’ll illustrate some of the characteristics of the data products, run through the single sensor products, say a bit more about the multisensory products: the LEO Infra-red CDR and the multi-sensor merged GEO LEO product.
I’ll end by outlining future developments in the final part of Phase 2.

## Slide 3: Consistent approach
CCI Calibration and Validation Database
  Perry, M. et al, Multisensor Thermal Infrared and Microwave Land Surface Temperature Algorithm Intercomparison. https://doi.org/10.3390/rs12244164
    Atmospheric profiles (ECMWF ERA-5)
    Surface emissivities (Combined ASTER and MODIS Emissivity for Land, CAMEL)
    Simulated TOA BTs (RTTOV)
  Database used in round robin exercise to select best algorithm for each product
  Database used in calculation of retrieval coefficients, error coefficients, and expected BTs for cloud masking
Common probabilistic cloud masking algorithm
Common auxiliary data (ERA-5, NDVI, FV, LCC)
ESA Land Cover Classification with further sub-division of bare soil class
Notes: We take a consistent approach across all the IR products, in fact all the LST CCI products.
We developed a CCI Calibration and Validation Database of atmospheric profiles and surface emissivities. The atmospheric profiles are selected from ERA-5 data in such a way as to represent the full range of physically real atmospheres. We use the CAMEL emissivities, again selecting to cover the likely range of emissivities of the Earth’s surface. These data together form a simulation Truth dataset. A radiative transfer model (RTTOV) is used to simulate the channel top-of-the-atmosphere brightness temperatures.
This database of profiles, surface emissivities, and TOA brightness temperatures was used in a round-robin exercise to select the best algorithm for each product. The database is also used for the calculation of the retrieval coefficients, error coefficients, and the expected brightness temperatures used in the cloud clearing algorithm.
We use a common cloud clearing algorithm across all the LEO infra-red products. The input auxiliary data is common to all products. We use the ESA Land cover classification as an input but with a modification – we have further subdivided the bare soil class with more soil types which increases the retrieval accuracy over some soil types.

## Slide 4: Phase 1 Single Sensor Products
Level 1 (swath, BTs) → Level 2P (LST, swath) → Level 3U (gridded, uncollated) → Level 3C (gridded, collated)
LST_cci polar orbiter, single IR sensor, products:
  Level 3C
All (single and multi sensor) LST_cci polar obiter, IR products:
  Regular equal-angle spatial grid.
  Day and Night in separate files.
  Temporal resolution: twice daily.
LST product updates in Phase 2:
  Extension of time series
  Reprocessing with CAMEL emissivity climatology
  Move to the latest reprocessing (4th) of data from ATSR-2 and AATSR
  STs over sea-ice
  Orbital drift correction variable added to NOAA AVHRR/3 products
  Introduction of new VIIRS LST products
  Terra MODIS V4.00, Aqua MODIS V4.00, ATSR-2 V4.00, AATSR V4.00, Sentinel 3A SLSTR V4.00, Sentinel 3B SLSTR V4.00, Metop-A AVHRR V2.00, NOAA15-19 AVHRR V1.50, SNPP VIIRS V1.00, NOAA20 VIIRS V1.00
Notes: If we move on to the processing of the data. We start with the brightness temperatures on the orbit swath, retrieve the LST on the swath and then the swaths are regridded onto a regular latitude-longitude grid. These swaths are then collated into day and night daily grids, keeping the swath pixel closest to the nominal overpass time. The monthly data are simply an average of the daily files. So all LEO IR single sensor products are level 3C.
The products are provided on equal-angle lat-lon spatial grids at the highest resolution permitted by the sensor: 0.01 degree or 0.05 degree depending on sensor.
Day and night products are provided in separate files. The temporal resolution is twice daily – one daytime and one nighttime file per day
In Phase 2 we extended the time series of the Phase 1 products. The CAMEL emissivity data were discovered to be unstable in time so the products have been reprocessed using a climatology instead. The ATSR-2 and AATSR products are derived from the 4th , latest, Reprocessing. The Phase 2 products include STs over sea-ice, cloud permitting. We have added an LST correction for orbital drift of the NOAA platforms. We have new products from VIIRS on NOAA20 and Suomi-NPP.
The products delivered in Phase 2 and currently available through the ESA Open Data Portal and the CEDA archive are LST from the MODIS instruments on Terra and Aqua, the Along-Track Scanning Radiometer 2, the Advanced Along-Track Scanning Radiometer, the Sea and Land Surface Temperature Radiometers on Sentinels 3A and 3B and the Advanced Very High Resolution Radiometer on Metop-A, from AVHRR on NOAAs 15 thru 19, and from VIIRS on NOAA20 and Suomi-NPP.

## Slide 5: Temporal Coverage
Notes: This plot shows the temporal coverage for each of the single sensor products and also the multisensor products.
Note there are temporal gaps in the ATSR-2 due to instrument failures.
We haven’t processed the MODIS data beyond 2021 as the platforms have been allowed to drift

## Slide 6: Spatial Coverage
Sun-synchronous, polar orbiters
  pass over or close to poles
  cross the equator at the same local solar time each day and night
Day/night defined by solar elevation
  poles – day data in summer, night data in winter
Coverage of IR data reduced by clouds
Terra MODIS
Daily, daytime
AATSR
Terra MODIS
Monthly, daytime
Notes: This slide will give you some idea of the kind of coverage you can get with the LEO IR products. On the right you have examples of a daily resolution nighttime grid from AATSR on Envisat at the top and Terra MODIS at the bottom. AATSR was a narrow swath sensor and so global coverage is achieved in 5 days where as MODIS gets near global coverage twice daily (so once daily for daytime, and once daily for nighttime).
We currently split our products by day and night on solar elevation so this means that coverage at the poles is seasonal.
Coverage of IR data is of course affected by clouds and you can see that even in the monthly plot on the left that there are some regions where there are no data for the whole month – this is July so the monsoon season in India, and the wet season over the Sahel.
Daily AATSR Night 2010/06/28
Daily MODISA Night 2018/07/20
Monthly MODISA Day 2018/07/01

## Slide 7: Uncertainties
Total uncertainty and a breakdown of the uncertainty budget into components based on error correlation:
uncertainty from uncorrelated errors
  lst_unc_ran
uncertainty from locally correlated errors on atmospheric scales
  lst_unc_loc_atm
uncertainty from locally correlated errors on surface scales
  lst_unc_loc_sfc
uncertainty from large-scale systematic errors
  lst_unc_sys
Notes: So if we move on to what you get in the products. As well as the LST we supply a total uncertainty at the pixel level and also a breakdown of the uncertainty budget by error correlation scale.
So one component for uncertainty arising from uncorrelated errors: such as instrument noise, sampling uncertainty.
uncertainty arising from errors correlated on atmospheric scale for instance errors in total column water vapour estimates.
the third component is uncertainty from errors correlated on surface scales such as geolocation errors.
Finally there is a term for large scale systematic errors such as radiative transfer model errors.

## Slide 8: Uncertainties
Correlated on surface scales
Uncorrelated
Large-scale
Correlated on atmospheric scales
Notes: These plots give you some idea of the relative scale of the uncertainty components. The component arising from uncorrelated errors is usually < 0.2 K. The locally correlated errors are somewhat larger, the systematic error is much smaller.
There will be a presentation from Claire Bulgin later with more information on how to use these uncertainties.

## Slide 9: NOAA Orbital Drift Correction
NOAA platform orbits not controlled – overpass time changes throughout mission
  can lead to spurious trends in LST
Radiative transfer model simulations of brightness temperatures at the observation and reference time
LST correction to reference time retrieved along with uncertainty
https://www.star.nesdis.noaa.gov/socd/sst/3s/
Notes: Some information about the correction to the LSTs for orbital drift of the NOAA platforms.
The overpass time changes throughout the missions for the NOAA platforms – obviously this is not good for climate studies as it will lead to spurious trends in the LST.
We have used radiative transfer simulations to estimate the difference between the BTs at the actual observation time and a reference time of 6am or 6pm local time. These are used to estimate the difference in LST at the two times and this is provided in the files as a correction to be added to the LST. The lst variable contains the uncorrected LST at the observation time and the dtime field also reflects the observation time.
The corrections are currently undergoing assessment.

## Slide 10: Multisensor IRCDR V3.00 (1995 - 2020)
Multisensor IRCDR comprises data from a series of instruments with a common heritage (ERS-2 ATSR-2, Envisat AATSR, Sentinel3B SLSTR) and the Terra MODIS.
Intercalibration between instruments is performed in brightness temperature (BT) space using the GSICS methodology.
  IASI (Infrared Atmospheric Sounding Interferometer) as reference
  IASI spectra convolved with sensor channel spectral response function.
  Resulting BTs matched with actual sensor BTs in time and space.
  Temperature dependent calibration applied.
Correct ATSR-2 and Terra MODIS times to 30 minutes earlier to align with AATSR and S3B SLSTR.
  Time correction is done in BT space (similar method to NOAA orbital drift correction).
  lst variable contains corrected LST
Terra MODIS 11 μm minus IASI
Instrument | EXT
ATSR-2 | 10:30
AATSR | 10:00
Terra MODIS | 10:30
SLSTR | 10:00
Notes: The first multi-sensor product I want to talk about is the Multi-sensor Infra red climate data record or IRCDR.
This is comprised of data from a series of instruments with a common heritage: the ATSR-2, AATSR, and SLSTR on Sentinel 3B. There was a time gap between AATSR and SLSTR. We use Terra MODIS to fill this gap as the overpass time is close to the other instruments.
When combining data from different sensors we must account for instrument calibration differences. Different sensors even if observing the same object through the same atmosphere would show small differences in observed temperatures due to calibration differences.
We do the intercalibration in brightness temperature space using a method based on the Global Space-based Inter-Calibration System method using IASI as a reference.
First, we calculate MODIS equivalent brightness temperatures by convolving the MODIS spectral response function with the IASI spectra. Then we match these in space and time with the actual MODIS brightness temperatures. In Phase 1 we used the operational IASI L1C data and estimated a time dependent calibration by doing a linear fit to the monthly average BT differences. [This is shown in the top plot for Terra MODIS 11 micron channel, the yellow line is the fit used for the calibration]. However, the operational IASI data uses different processors at different times so contains instabilities. Also, as the IASI data are not available before 2007 we had to extrapolate back in time. In Phase 2 we have used the IASI FCDR which accounts for the processor changes and we have instead used a temperature dependent calibration [this shown in the bottom plot which shows small temperature dependency ].
We have applied the calibration to the MODIS instruments. We don’t apply a calibration to the SLSTRs as the offset against IASI is very small, an order of magnitude smaller than its uncertainty.
You can see from the table that there is a half-hour difference between the overpass times of AATSR SLSTR and Terra MODIS so we must apply a correction for this time difference otherwise we would likely end up with non-climatic step changes in the record.
We use MODIS as the reference and correct to 10:30. The correction is calculated in LST space so using matchups between the two instruments. and calculating a straight line fit to the LST difference as a function of observation time difference. The correction was banded by day-night, land-cover class, and latitude band. The plots show an example of the matchup difference v. time difference for daytime and nighttime. Note, these matchups were calculated before the intercalibration was applied to the MODIS data which is why the LST difference is non-zero at zero time difference. For the morning overpasses, the earlier instrument observes colder temperatures, whilst at night the reverse is true and the LST differences are much smaller which is as expected.
The IRCDR runs from 1995 – 2025. For consistency, we have kept the reduced swath width of the ATSRs for the whole time series.

## Slide 11: Multisensor IRMGP
3 hourly, on 0.05grid
Based on a merged GEO product with added LEO LST outside of GEO footprint
30 minute window
Coverage will vary:
  during time series, and at different times of day because of different satellites available
2018-07-01
06:00 UTC
18:00 UTC
Notes: the second multi-sensor product is the merged GEO LEO product. This is based on a merged GEO product produced by Sofia and colleagues at IPMA.
the product is 3 hourly on a 0.05 degree grid.
Data from ATSR-2,AATSR,SLSTR and MODIS are included outside of the footprint of the GEOS if the observations lie within a 30 minute window around the time of the product. this time window was chosen to be in line with the typical scan periods of the GEO sensors.
For this product a common algorithm is preferred so the LEOS are processed with a Generalized Split Window Algorithm as are the GEOs unless they don’t have the required channels and a single channel retrieval is used.
The coverage of this product will vary throughout the time series depending on which sensors are available.
The product may be suitable for diurnal studies.

## Slide 12: Updates in IRCDR V3.5
instruments: ATSR-2, Terra MODIS, S3B SLSTR
further intercalibration to improve longterm stability:
  ATSR-2 and SLSTR with Terra MODIS as reference
  using ERA 5 skin temperature as proxy
swath collation: ascending (22:00) / descending swath (10:00)
swath width: maximum satellite zenith angle 35°(was 22°)

## Slide 13: Data Access
Data Access
  ESA Open Data Portal
    https://climate.esa.int/en/data/#/dashboard
  CEDA Catalogue
    https://catalogue.ceda.ac.uk/ (search for “lst cci”)
Key Documents
  https://climate.esa.int/en/projects/land-surface-temperature/
  Product User Guide
  Algorithm Theoretical Basis Document
  End-to-End ECV Uncertainty Budget
  Product Validation and Intercomparison Report
  among others
Notes: to end the products can be accessed through the ESA Open Data Portal or CEDA if you have access
key documents can be found on the project website:
Thank you