## Slide 1
Microwave LST_cci Product
Carlos Jimenez, Catherine Prigent, Iris de Gelis
Estellus, Paris Observatory

## Slide 2: Microwave remote sensing
Microwave (MW) emission from the Earth’s surface at much longer wavelengths than in the infrared (IR) can also be used to estimate the land surface temperature (LST). However, the energy emitted (E) is weaker and is less sensitive to changes on the emitting temperature (T).
E ~ T4 E ~ T

## Slide 3: Microwave observations EMISSIVITY
eIR[8.3um]
eMW[19GHz-hpol]
The radiant temperature (TR) has also a larger dependence on the emissivity (e), which has a larger variability than in the IR, changing with the surface conditions (e.g., the state of the vegetation, the soil moisture content).
TR = eIR1/4 T
TR = eMW T

## Slide 4: Microwave observations EMITTING TEMPERATURE
Longer wavelengths have larger penetration depth; in very arid places MWs observe a emitting temperature integrated over a few cms below the surface, differing from the skin temperature measured in the IR.
emitting depth at 18 GHz
Favrichon et al., 2021, ﻿https://doi.org/10.3390/ rs13071325

## Slide 5: Microwave observations SPATIAL RESOLUTION
Weaker emission and longer wavelengths require large antennas, resulting in relatively large measurement footprints on the ground, in the order of tens of kms.
~25 km

## Slide 6: Microwave observations CLOUDS
At the observing MW window channels the land surface emission traverses most of the clouds, therefore LST can be estimated for most weather conditions and does not suffer from the “clear-sky bias” of the IR measurements.

## Slide 7: MW LST product SENSORS
SSM/I | SSMIS | AMSR-E | AMSR2
Frequency & Resolution |  |  | 
19.35 GHz (69x43 km) | 19.35 GHz (73x47 km) | 18.7 GHz (27x16 km) | 18.7 GHz (14x22 km)
23.235 GHz (50x40 km) | 23.235 GHz (73x47 km) | 23.8 GHz (32x18 km) | 23.8 GHz (15x26 km)
37.0 GHz (37x28 km) | 37.0 GHz (41x31 km) | 36.5 GHz (14x8 km) | 36.5 GHz (7x12 km)
85.5 GHz (15x13 km) | 91.5 GHz (14x13 km) | 89.0 GHz (6x4 km) | 89.0 GHz (3x5 km)
Nominal Incident Angle |  |  | 
53o | 53o | 55o | 55o
Swath width |  |  | 
1400 km | 1700 km | 1450 km | 1450 km
Nominal Equator Crossing Local Time |  |  | 
6 am/pm | 6 am/pm | 1.30 am/pm | 1.30 am/pm
Satellite Platform |  |  | 
DMSP F13 | DMSP F17 | Aqua | GCOM-W1
Period |  |  | 
1996-2008 | 2008-2024 | 2003-2011 | 2013-2024
SSM/I and SSMIS radiances sourced from the Satellite Application Facility on Climate Monitoring (CM-SAF) FCDR of inter-calibrated brightness temperatures
AMSR-E and AMSR2 from the Precipitation Processing System (PPS) Public Archive
https://pps.gsfc.nasa.gov
https://www.cmsaf.eu/EN/Overview/OurProducts/FCDR/FCDR_node

## Slide 8: MW LST product DATA RECORDS
~25 km
SSM/I
Spatial Resolution
Time of day
Years
1996
2024
2003
2008
2011
2013
SSMIS
AMSR-E
AMSR2
SSMIS
AMSR2
~12 km
~5 km
[gridded at 0.125o]
[gridded at 0.125o]
[gridded at 0.05o]
SSM/I
SSMIS
at observing time
corrected to 6AM/PM
at ~1.30 AM/PM
at observing time
PROTOTYPE

## Slide 9: MW LST product DATA RECORDS
~25 km
SSM/I
Spatial Resolution
Time of day
Years
1996
2024
2003
2008
2011
2013
SSMIS
AMSR-E
AMSR2
SSMIS
AMSR2
~12 km
~5 km
[gridded at 0.125o]
[gridded at 0.125o]
[gridded at 0.05o]
SSM/I
SSMIS
at observing time
corrected to 6AM/PM
at ~1.30 AM/PM
at observing time
PROTOTYPE

## Slide 10: MW LST product TEMPORAL RESOLUTION
2006/06/06
SSM/I ~6AM
- FX polar satellites, so twice per day, with a sensor swath of ~ 1400 – 1700 km.
By processing SSM/I, SSMIS, AMSR-E and AMSR2 the data record can sample the LST diurnal cycle 4 times per day.

## Slide 11: MW LST product TEMPORAL COVERAGE
- Swath width resulting in coverage of ~50% at the equator (due to the ~2 days revisiting time), increasing toward the poles (overlapping swaths).
MODIS 1.30AM coverage
SSMIS 6AM coverage
- LST available under most cloudy conditions, but deep convective clouds identified and LST flagged out (surface radiation scattered away by ice cloud particles at 37 GHz).

## Slide 12: MW LST product UNCERTAINTY
12 km
simulated SSM/I footprint
Evora LST station
Larger than for the IR LST due to the more varying emissivity, with estimated uncertainty in the order of 2-4K.
Comparison with station data can show larger differences, partly due to the terrain inhomogeneity at the ~25km resolution.
Uncertainty 2010/01/01 6AM (K)

## Slide 13: MW LST product DATA RECORDS
~25 km
SSM/I
Spatial Resolution
Time of day
Years
1996
2024
2003
2008
2011
2013
SSMIS
AMSR-E
AMSR2
SSMIS
AMSR2
~12 km
~5 km
[gridded at 0.125o]
[gridded at 0.125o]
[gridded at 0.05o]
SSM/I
SSMIS
at observing time
corrected to 6AM/PM
at ~1.30 AM/PM
at observing time
PROTOTYPE

## Slide 14: MW LST product TEMPORAL CORRECTION
The FX satellites do not have a system to stabilize their orbits, so orbit injection and orbital drift affect the observing local time. F13 and F17 are selected to minimize the change in observing local time, and an optional LST correction to homogenize the record to a 6AM/PM overpass is also provided.

## Slide 15: MW LST product TEMPORAL CORRECTION
No correction for AMSR-E and AMSR2 needed, no “drift” as for SSMI, but notice that for all LEO sensors there is always a “modulation” of the observing local time due to the observation swath and orbit particularities.
1.30AM
~20o ~= 1 ½ hours

## Slide 16: MW LST product STABILITY ASSESMENT
Testing data record stability by differences in monthly time anomalies between CRUTEM land-surface air temperature and the MW LST
GCOS LST requirements

## Slide 17: MW LST product STABILITY ASSESMENT
Testing data record stability by differences in monthly time anomalies between CRUTEM land-surface air temperature and the MW LST
GCOS LST requirements

## Slide 18: MW LST product DATA RECORDS
~25 km
SSM/I
Spatial Resolution
Time of day
Years
1996
2024
2003
2008
2011
2013
SSMIS
AMSR-E
AMSR2
SSMIS
AMSR2
~12 km
~5 km
[gridded at 0.125o]
[gridded at 0.125o]
[gridded at 0.05o]
SSM/I
SSMIS
at observing time
corrected to 6AM/PM
at ~1.30 AM/PM
at observing time
PROTOTYPE

## Slide 19: MW LST product DOWNSCALED LST
Downscaling method to offer a MW LST product at 5km resolution, prototype completed.
downscaling
AMSR2 1AM
AMSR2 1PM
SSMI 6AM
SEVIRI 1AM
SEVIRI 1PM
SEVIRI 6AM
MODIS 1AM
MODIS 1PM
Original 25km – 12.5km
Downscaled 5km
evaluating
example in Southern Ethiopia
- based on Favrichon et al. A method to downscale satellite microwave land-surface temperature. Remote Sens., 13(7):1325, 2021, paper with updated methodolgy an evaluation on their way.

## Slide 20: MW LST product SUMMARY
~25 km
SSM/I
Spatial Resolution
Time of day
Years
1996
2024
2003
2008
2011
2013
SSMIS
AMSR-E
AMSR2
SSMIS
AMSR2
~12 km
~5 km
[gridded at 0.125o]
[gridded at 0.125o]
[gridded at 0.05o]
SSM/I
SSMIS
at observing time
corrected to 6AM/PM
at ~1.30 AM/PM
at observing time
PROTOTYPE
Newest version 6.01 including SSMIX and AMSRX LST about to be made publicly available at the CEDA archive.