## Slide 1
Uncertainties in the LST_cci products
Claire Bulgin
University of Reading, National Centre for Earth Observation

## Slide 2: Background
Every measurement we make (both in-situ or remotely sensed) deviates from the ‘true’ surface temperature due imperfections in the instrumentation and measurement process. The uncertainty information helps you to make the best use of the data, particularly in a decision-making context.
Error and uncertainty are two different concepts…
Error: How different is the measured value from the true value?
Uncertainty: To what degree is the measured value in doubt?
Measurement error is typically unknown (if we did know what it was, we would correct for it). We therefore estimate the distribution of possible measurements around the true value. The differences between these measurements and the true value gives the error distribution and the width of this is the uncertainty.

## Slide 3: Diurnal cycle in LST (1)
Research question: What is the diurnal cycle in LST on a given day over this part of the African continent?
0000
2400
1200
280 K
330 K

## Slide 4: Diurnal cycle in LST (2)
0000
2400
1200
280 K
330 K
Tmax
Tmin
Diurnal
Range
Research question: What is the diurnal cycle in LST on a given day over this part of the African continent?

## Slide 5: Diurnal cycle in LST (3)
0000
2400
1200
280 K
330 K
Research question: What is the diurnal cycle in LST on a given day over this part of the African continent?

## Slide 6: Diurnal cycle in LST (4)
0000
2400
1200
280 K
330 K
Tmax
Tmin
Diurnal
Range
Research question: What is the diurnal cycle in LST on a given day over this part of the African continent?

## Slide 7: Quality level ‘vs’ uncertainty
Quality level
Uncertainty
Typically tells you about failure or success or one or more aspects of the measurement process e.g.
Was the data provided from the instrument good quality or complete?
Did the retrieval process run without error?
Was the retrieval done under optimal conditions?
Was all the required auxiliary data available?
Quality levels might be calculated as some aggregation of all of the above information.
Tells you about the degree of doubt in the measurement provided e.g.
Keeps track of the uncertainties from different error sources throughout the retrieval process (not just the outcome of a single decision point).
Provides some indication of the weight you should place on a given measurement in a decision weighting process – it’s not a ‘yes/no’ flag.
Properties of uncertainties mean that it can evolve if you derive new products.

## Slide 8: Why using uncertainty correctly is important
Imagine that you wanted to take a monthly LST product and re-grid this from 0.05 to 0.25 degree resolution:
h
Warmer
Cooler
LST
LST averages over the region of interest.

## Slide 9: Quality level ‘vs’ uncertainty
Quality level
Uncertainty
Typically tells you about failure or success or one or more aspects of the measurement process e.g.
Was the data provided from the instrument good quality or complete?
Did the retrieval process run without error?
Was the retrieval done under optimal conditions?
Was all the required auxiliary data available?
Quality levels might be calculated as some aggregation of all of the above information.
Tells you about the degree of doubt in the measurement provided e.g.
Keeps track of the uncertainties from different error sources throughout the retrieval process (not just the outcome of a single decision point).
Provides some indication of the weight you should place on a given measurement in a decision weighting process – it’s not a ‘yes/no’ flag.
Properties of uncertainties mean that it can evolve if you derive new products.

## Slide 10: Why using uncertainty correctly is important
Imagine that you wanted to take a monthly LST product and re-grid this from 0.05 to 0.25 degree resolution:
Warmer
Cooler
LST
Uncertainties
Larger
Smaller
LST averages over the region of interest.

## Slide 11: Why using uncertainty correctly is important
Imagine that you wanted to take a monthly LST product and re-grid this from 0.05 to 0.25 degree resolution:
Warmer
Cooler
LST
Uncertainties
Larger
Smaller
Propagated uncertainty at the target resolution is reduced as many error sources are uncorrelated at this scale.
LST averages over the region of interest.

## Slide 12: Why using uncertainty correctly is important
Imagine that you wanted to take a monthly LST product and re-grid this from 0.05 to 0.25 degree resolution:
x
x
x
x
x
x
x
x
x
x
x
x
Warmer
Cooler
LST
Uncertainties
Larger
Smaller
Propagated uncertainty at the target resolution is reduced as many error sources are uncorrelated at this scale.
LST averages over the region of interest.
Thresholding uncertainties

## Slide 13: Why using uncertainty correctly is important
Imagine that you wanted to take a monthly LST product and re-grid this from 0.05 to 0.25 degree resolution:
Warmer
Cooler
LST
Uncertainties
Larger
Smaller
Propagated uncertainty is smaller…
…but you are adding sampling uncertainty by removing data.
Excluding data changes the mean LST over the region of interest.
Thresholding uncertainties

## Slide 14: Uncertainties provided for all products
MODIS, 10:30am overpass
LST
Total uncertainty
SSMI, 6.30am overpass

## Slide 15: Breakdown of uncertainty components
Why do we provide this breakdown?
The main reason is so that users can use our data to create new products e.g.
Coarsening data for comparison with model output.
Calculating area averages over cities or regions of interest.
Correlation length scale indicates whether these uncertainties average down when propagated.

## Slide 16: How do I find out more?
Weds 13th May at 10:00: UCS#3 Changes in LST over rural and urban areas (Panagiotis Sismanidis).
Thurs 14th May at 10:35-12:15: LST_cci drop in session.
LST_cci documentation:
  Product user guide
  End-to-end ECV uncertainty budget