## Slide 1
UCS#2: Assessment of ESA LST_cci Sea-Ice Surface Temperatures (IST) in the Arctic
Pia Englyst, Adrien Combelles, Ugo Halmaert, Ioanna Karagali

## Slide 2: Introduction
DMI a Production Unit (PU) for Copernicus Marine Service
Products delivered for the Sea Ice Thematic Assembly Center (TAC)
  Near-Real-Time SEAICE SST/IST L4 (011_008) and L3S (011_022)
  Multi-Year SEAICE SSR/IST L4 (011_016) and L3S (011_040)
Ocean Monitoring Indicators https://data.marine.copernicus.eu/product/OMI_CLIMATE_SST_IST_ARCTIC_anomaly/description

## Slide 3: MY L4 SST/IST product overview
Input data:
  ESA SST_cci L3U SST (1982-2021)
  C3S ICDR L3U SST (2022-)
  AASTI v2.1 IST CDR (1982-Jul 2019)
  C3S v1.0 IST CDR (July 2019-2022)
  C3S v1.1 ICDR (2023-onwards)
OSI SAF Sea Ice Concentration to identify sea ice.
Input data processed using an IST, SST or MIZ algorithm.
Described in Nielsen-Englyst P. et al., A combined sea and sea-ice surface temperature climate dataset of the Arctic 1982-2021, Rem Sens Env, 284, 113331, https://doi.org/10.1016/j.rse.2022.113331

## Slide 4: Example
Example of L3S and L4 OI IST/SST product along with the surface mask and uncertainty estimates*. Observed stability: −0.0001 °C/yr and 0.0047 °C/yr against drifters (SST) and NP (IST) observations*. *Nielsen-Englyst P. et al., A combined sea and sea-ice surface temperature climate dataset of the Arctic 1982-2021, Rem Sens Env, 284, 113331, https://doi.org/10.1016/j.rse.2022.113331

## Slide 5: UCS#2 Aims and Approach
Use ESA LST_cci IST Level 2 form SLSTR on S3-A/B and MODIS on Aqua/Terra
Produce Level 3 collated (L3C) single-sensor products (SSP) for each sensor/platform
Assess L3C SSP using
  in situ observations from the Seasonal Ice Mass Balance Buoys 3 (SIMB3)
  in situ observations from the Qaanaaq Automatic Weather Station on the sea ice (-69.133°E, 77.427°N in 2021)
  AASTI v2.1 IST Climate Data Record (CDR) and Interim CDR (ICDR), available through C3S from 1982 onward.
Ingest ESA LST_cci L3C SSP in Copernicus Marine Service Arctic L4 SST/IST Multi-Year Product https://doi.org/10.48670/moi-00123

## Slide 6: List of LST_cci products used for UCS#2
Use ESA LST_cci IST Level 2 form SLSTR on S3-A/B and MODIS on Aqua/Terra
*For CCN5 the submitted manuscript received revisions related to the period of assessment (only 2021) thus in CCN6, USC#2 was rescoped to extend the period.
Product String and version | Sensor type | Resolution | CCN5 period | CCN6 period
AQUA MODIS L2P v4.aa | IR | 1 km at nadir | 2021 | 2019-2020*
TERRA MODIS L2P v4.aa | IR | 1 km at nadir | 2021 | 2019-2020*
Sentinel 3A SLSTR L2P v4.aa | IR | 1 km at nadir | 2021 | 2019-2023*
Sentinel 3B SLSTR L2P v4.aa | IR | 1 km at nadir | 2021 | 2019-2023*

## Slide 7: Validation Strategy
Using in situ observations
  of T2air from Seasonal Ice Mass Balance Buoy 3 (SIMB3) for SSP and L4 SST/IST
  of T2air and IST from the automated Qaanaaq weather station for L4 SST/IST
In situ SIMB3 stations in 2021 and Qaanaaq AWS

## Slide 8: Example of input data, L3S & L4 SST/IST: 16/05/21
Input data
  MODIS
  SLSTR
  AASTI (AVHRR based)
Output L3S and L4 SST/IST
.

## Slide 9: Validation Results for SSP, 2021
Lowest mean bias and RMS against SIMB3 for MODIS/T.
The L3 Super-Collated DMI product shows the lowest standard deviation.
Product | Mean Bias | Standard Deviation | RMS | Match-ups
MODIS/Aqua | -1.39 | 2.57 | 2.92 | 734
MODIS/Terra | -1.07 | 2.42 | 2.64 | 604
SLSTR/S3-A | -1.90 | 2.31 | 2.99 | 847
SLSTR/S3-B | -2.18 | 2.52 | 3.33 | 725
AASTI v2.1 | -2.12 | 2.88 | 3.57 | 808
L3S MY SST/IST | -1.98 | 2.20 | 2.96 | 1022

## Slide 10: Validation Results for L4 SST/IST, 2021
Positive impact of ingesting LST_cci IST as data availability increases and validation of L4 SST/IST is improved.
L4 SST/IST version | Mean Bias |  |  | Standard Deviation |  |  | RMS |  |  | Match-ups |  | 
 | SIMB3 | QAIR | QIST | SIMB3 | QAIR | QIST | SIMB3 | QAIR | QIST | SIMB3 | QAIR | QIST
Reference | -2.66 | -3.18 | -2.01 | 2.84 | 3.31 | 3.45 | 3.89 | 4.58 | 3.98 | 1091 | 156 | 156
Updated | -2.06 | -2.91 | -1.73 | 2.16 | 2.53 | 2.77 | 2.98 | 3.85 | 3.26 | 1092 | 156 | 156

## Slide 11: Impact on estimated uncertainties
Difference is mostly negative suggesting lower uncertainty in the updated L4 SST/IST using LST_cci.
L4 IST Uncertainty from reference SST/IST product
Difference in IST Uncertainty between updated and reference SST/IST

## Slide 12: Current status on In Situ Data
SIMB3 2019-2023 (Tair)
MOSAiC (Tair & IST)
.

## Slide 13: Status
A paper was submitted in RSE on August 14, 2025
A point for major review was to extend the analyses to more years beyond 2021
Thus, the extension UCS#2 for CCN6 was rescoped to cover the period 2019-2023 using SLSTR-A/B L2P and MODIS-A/T.
The rationale is to cover the period of the available in situ observations from the MOSAiC Expendition (2019-2020) and to increase the availability of SIMB3 observations.
Currently the L2P LST_cci data are being generated/downloaded in order to be prepared for further analyses.