## Slide 1
Super Extreme LST Hotspots
Lizzie Good, Josh Blannin (Met Office)
Abigail Waring, Karen Veal, Darren Ghent (U. Leicester)

## Slide 2: Overview
Article in Bulletin of the American Meteorological Society (BAMS) State of the Climate (SotC) Global Chapter
‘Super extreme land surface temperature hotspots
Demonstrate how LST data could be used to characterise and monitor ‘Super Extreme Hotspots’ (SEH)
https://ametsoc.net/sotc2024/02GlobalClimate_SotC2024.pdf

## Slide 3: Background to the study
Well documented that as the Earth’s climate warms, the frequency of extreme heat events is increasing (IPCC, 2021, Dunn et al., 2024, Willett, 2023).
Evidence suggests that the fraction of land becoming uninhabitable due to extreme heat will also increase with global warming (Matthews et al., 2025).
Surface temperatures are traditionally monitored using data from weather stations measuring near-surface air temperature at ~1.5-2m above the surface (T2m). However, station density and location limit spatial coverage and therefore knowledge of how extreme temperature frequency and intensity is evolving in many regions of the world (Dunn et al., 2024; also see Robert Dunn’s presentation on Wednesday afternoon).
Distribution of HadEX3 stations for TXx (Dunn et al, 2020)
Dunn, et al. (2020), Development of an updated global land in-situ-based dataset of temperature and precipitation extremes: HadEX3, JGR-A, 125, e2019JD032263
Dunn et al (2024): Surface Temperature Extremes [in “State of the Climate in 2023”]. Bull. Amer. Meteor. Soc, 105 (8), S37-S39 https://doi.org/10.1175/BAMS-D-24-0116.1.
IPCC. (2021). In V. Masson-Delmotte, P. Zhai, A. Pirani, S. L. Connors, C. Péan, S. Berger, et al. (Eds.), Climate change 2021: The physical science basis. Contribution of working group I to the sixth assessment report of the intergovernmental panel on climate change. Cambridge University Press. Retrieved from https://www.ipcc.ch/report/sixth-assessment-report-working-group-i/
Matthews et al. (2025): Mortality impacts of the most extreme heat events. Nat Rev Earth Environ (2025). https://doi.org/10.1038/s43017-024-00635-w
Willett (2023) HadISDH.extremes Part II: Exploring humid heat extremes using wet bulb temperature indices. Adv. Atmos. Sci.,40, 1968–1985, https://doi.org/10.1007/s00376-023-2348-7.
Notes: Leicester to run the regridding tool – e.g. 0.25 degs.

## Slide 4: Can we monitor global hotpots using LST?
Step 1: Ensure LST record is stable over time – critical for any monitoring activity (see my talk on Wednesday pm). Note data from 2024 required for BAMS SotC.
Test this using a stable dataset that has similar properties – using CRUTEM5 T2
Step 2: Does LST show the same spatial patterns as T2m? What information useful information can we get from satellite LST?
Step 3: Detect hotspots in global, multi-year LST data
Step 4: Monitor hotspots over time (to be done)
This talk

## Slide 5: Step 1: Temporal stability of the LST data
Trend 0.45 K/decade
P-value > 0.05
Trend -0.08 K/decade
P-value < 0.05
SLSTR/B – CRUTEM5
(limited ±60 lat)
SLSTR/A – CRUTEM5
(limited ±60 lat)
  Verify temporal stability of the LST data used in the study
  CRUTEM5 used as stable reference –based on monthly, homogenised station data (where non-climatic discontinuities have been removed.
  LST data from LST_cci
  SLSTR-A unstable
  SLSTR-B stable
  Cannot use SLSTR-A for any time series analysis
CRUTEM5: Osborn et al. (2020), Land surface air temperature variations across the globe updated to 2019: the CRUTEM5 dataset, J. Geophys. Res. doi: 10.1029/2019JD032352

## Slide 6: Step 2: What information does LST provide?
Very consistent spatial relationship between LST and T2m anomalies
  SLSTR/B and CRUTEM5 anomalies are spatially well correlated.
  Maps are for April 2024 Pearson correlation coefficient r = 0.84 => spatially well correlated
  r=0.81 for global monthly time series
  SLSTR/B more complete spatial coverage

## Slide 7: Step 2: What information does LST provide?
The percentiles from the 2024 distribution of maximum LSTs are:
50.5 degC (95th)
57.7 degC (99th)
62.3 degC (99.9th)
The hottest LSTs above ~62 degC often occur in isolated grid cells and are associated with lava flows or wildfires.
LSTs > 50 degC are moderately extreme!
LSTs > 55 degC are extreme!
Maximum LST observed during 2024 by SLSTR/B at 0.01 latitude-longitude. White areas represent 0.01°grid cells with no valid data in this year (e.g. due to persistent cloud or water bodies).

## Slide 8: Step 3: Detect Super Extreme LST Hotspots
Using only full-year daytime data between 2019 and 2024, thresholds of 50 degC & 55 degC used to identify SEHs
SEHs prevalent in the Arabian peninsula, Iran (Lut desert), across central Asia, parts of North Africa, North West USA, North Mexico and Australia.
General consistent with previous studies (e.g. using MODIS LST data; note MODIS cannot be used here as the data are unstable after 2021 due to orbital drift).
Map showing where two or more valid SLSTR/B LSTs observations in 2024 exceed selected LST thresholds (25, 30, 35, 40, 45, 50 and 55°C), resampled to 0.1° latitude-longitude.
Notes: Full-year daytime data 2019 and 2024: thresholds of 50°C and 55°C are used to identify SEHs (55°C is above the 99th percentile for the 2019-2024 SLSTR-B data: 53.2°C).
For all SEH metrics 2019 is ranked as the most extreme year. For the number of SEH locations, 2024 ranks 4th (55°C) and 5th (50°C), while for the aggregated annual fractions, 2024 ranks 2nd.

## Slide 9: Step 3: Detect Super Extreme LST Hotspots
Total number of grid cells exceeding thresholds each year
Total fraction of valid observations across all grid cells exceeding each threshold
Count occurrences of 0.1 °grid cell LSTs exceeding threshold temperatures of 50 and 55 degC
Plot time series of exceedances
Total number => annual time series of the number of SEH locations
Total fractional sum => accumulated global frequency of SEHs each year
Trends statistically insignificant – need longer time series! 6 years too short.

## Slide 10: Summary
Satellite LST data from SLSTR-B has been used to identify ‘global super extreme hotspots (SEH)’
These hotspots likely correspond to the hottest places on Earth and could indicate where the Earth is /has become uninhabitable for humans (and other wildlife)
The current time series of SLSTR-B LST_cci data are too short for monitoring
Currently there are no real-time, long-term LST datasets suitable for global, real-time monitoring of hotspots (hopefully VIIRS, and SLSTR-A will be when stable)
  Restricted to using climate-quality dataset including most recent year in BAMS (in this case, 2024). Only SLSTR/B LST_cci data currently fulfils this requirement.

## Slide 11: Next Steps
Extend analysis to other LST_cci datasets (temporally stable ones only), including those with no up-to-date data, e.g. for past year or so.
Compare results between sensors – hopefully consistent. Longer time series will reveal any statistically significant changes in hotspots location and frequency.
This information will be useful for identifying new and evolving hotspots, where the risk is high for the land being uninhabitable.
Good, E.; Blannin, B.; Waring, A.; Veal, K.; Ghent, D. Sidebar 2.1: Super extreme land surface temperature hotspots. In State of the Climate in 2024; American Meteorological Society: Boston, MA, USA, 2025; Volume 106, pp. S37–S39. https://doi.org/10.1175/BAMS-D-25-0102.1