## Slide 1: Using satellite LST in climate science applications
Lizzie Good (Met Office, LST_cci)

## Slide 2: Some things to bear in mind using LST…

## Slide 3: What we have already heard about
Different data sources – different datasets are good for different applications.
Uncertainties in LST data and how to use them
Validation results confirm the accuracy and precision of LST datasets, and the accuracy of uncertainties
Coverage
Temporal stability
Existing user studies can provide good examples of use cases, and how to use the data

## Slide 4: Consider the spatial coverage
Be aware that coverage is not 100%
Gaps between swaths for all sensors (especially at lower latitudes)
Gaps for applications that require clear sky
Figures source: LST_cci PUG
Figures source: Carlos Jiménez, Estellus

## Slide 5
Also consider temporal coverage
Daily/monthly/annual means may comprise either one or more observations period – not all times are observable (particularly for IR observations).
Temporal means biased to certain weather conditions => clear-sky bias
10am/pm observation time

## Slide 6: Why using uncertainty correctly is important
Imagine that you wanted to take a monthly LST product and re-grid this from 0.05 to 0.25 degree resolution:
Warmer
Cooler
LST
LST averages over the region of interest.
Figures source: Claire Bulgin, U. Reading

## Slide 7: Why using uncertainty correctly is important
Imagine that you wanted to take a monthly LST product and re-grid this from 0.05 to 0.25 degree resolution:
Warmer
Cooler
LST
Uncertainties
Larger
Smaller
LST averages over the region of interest.

## Slide 8: Why using uncertainty correctly is important
Imagine that you wanted to take a monthly LST product and re-grid this from 0.05 to 0.25 degree resolution:
Warmer
Cooler
LST
Uncertainties
Larger
Smaller
Propagated uncertainty at the target resolution is reduced as many error sources are uncorrelated at this scale.
LST averages over the region of interest.

## Slide 9: Why using uncertainty correctly is important
Imagine that you wanted to take a monthly LST product and re-grid this from 0.05 to 0.25 degree resolution:
x
x
x
x
x
x
x
x
x
x
x
x
Warmer
Cooler
LST
Uncertainties
Larger
Smaller
Propagated uncertainty at the target resolution is reduced as many error sources are uncorrelated at this scale.
LST averages over the region of interest.
Thresholding uncertainties

## Slide 10: Why using uncertainty correctly is important
Imagine that you wanted to take a monthly LST product and re-grid this from 0.05 to 0.25 degree resolution:
Warmer
Cooler
LST
Uncertainties
Larger
Smaller
Propagated uncertainty is smaller…
…but you are adding sampling uncertainty by removing data.
Excluding data changes the mean LST over the region of interest.
Thresholding uncertainties

## Slide 11: Instability: Orbital Drift (1)
Figures source: https://www.remss.com/
Orbits take ~100 minutes -> approximately 14 orbits per day
Some satellite overpasses drift with time – critical for some variables with diurnal variability, e.g. LST
AVHRR – TIROS-N, NOAA-6/8/10
AVHRR/2 – NOAA-7/9/11/12/13/14
AVHRR/3 – NOAA-15/16/17/18/19, Metop-A/B/C
Instability: Orbital Drift (1)

## Slide 12: Instability: Orbital Drift (2)
LST_cci MW data. Pseudo-global (Antarctica excluded) interannual monthly anomaly, time correction not applied (V2.33)
LST has a strong diurnal and seasonal cycle
F13
F17
Figures source: Carlos Jiménez, Estellus

## Slide 13: Instability: Orbital Drift (3)
Pseudo-global (Antarctica excluded) interannual monthly anomaly, time correction applied LST_cci MW LST (v2.33).
F13
F17
Figures source: Carlos Jiménez, Estellus

## Slide 14: Instability: Input Data
Instability can also result from the input data used in retrievals
Combined ASTER and MODIS Emissivity database over Land (CAMEL) – widely used!
Produced by U. Wisconsin + NASA JPL
Analysis shows global time series of data are not stable
CAMEL Version 3
Figure source: Sofia Ermida, IPMA
CAMEL Version 2
Input data includes satellite radiances, emissivity (veg, land cover), water vapour, clouds…..

## Slide 15: From UCS#4: Super Extreme Land Surface Temperature Hotspots (presentation earlier)
Trend 0.45 K/decade
P-value > 0.05
Trend -0.08 K/decade
P-value < 0.05
SLSTR/B – CRUTEM5
(limited ±60 lat)
SLSTR/A – CRUTEM5
(limited ±60 lat)
  Verify temporal stability of the LST data used in the study
  CRUTEM5 used as stable reference –based on monthly, homogenised station data (where non-climatic discontinuities have been removed.
  SLSTR-A not stable due to input radiances available from ESA.
CRUTEM5: Osborn et al. (2020), Land surface air temperature variations across the globe updated to 2019: the CRUTEM5 dataset, J. Geophys. Res. doi: 10.1029/2019JD032352
Key Message: Check Stability!!!

## Slide 16
Where to find information from LST_cci

## Slide 17: LST_cci webpages – Key Documents
Product User Guide (PUG)
Many other documents for further info, e.g. Algorithm Theoretical Basis Document, End-to-End Uncertainty Budget, Product Intercomparison and Validation Report, Climate Assessment Report

## Slide 18: LST_cci webpages – Data, Tool, …
Links to
‘Tool’ (Regridding and Subsetting Tool)
‘Data’ - includes ‘issues & updates log’)
Link to issues & updates log.

## Slide 19: Issues and updates log (linked from ‘Data’)

## Slide 20: Relationship Between LST and T2m

## Slide 21: LST can Complement T2m
Station air temperature ~2m (T2m) widely used to monitor climate change, quantify extremes, validate climate models, attribution studies, …
However, station network is sparse
CRUTEM4 (http://www.metoffice.gov.uk/hadobs)
NB: CRUTEM4 superseded by CRUTEM5
Source: National Centers for Environmental Information (NCEI)

## Slide 22: LST vs T2m Correlation
LST vs T2m instantaneous correlation is typically very high (often >0.9)
LST vs T2m anomalies* can also be very high (particularly when at low spatio-temporal resolution)
Anomalies = obs - climatology
Good et al., 2017, A spatio-temporal analysis of the relationship between near-surface air temperature and satellite land surface temperatures using 17 years of data from the ATSR series, J. Geophys. Res. Atmos., doi:10.1002/2017JD026880)

## Slide 23: T2m vs LST (1)
Good, E. J. (2016), An in situ-based analysis of the relationship between land surface “skin” and screen-level air temperatures, J. Geophys. Res. Atmos., 121, 8801–8819, doi:10.1002/2016JD025318.
Niamey 02/09/06
Niamey 09/06/06
Cape Cod 21/06/13
Oklahoma 26/03/14
Oklahoma 30/11/14
Azores 25/06/14
Analysis between colocated in situ LST and T2m at Atmospheric Radiation Measurement (ARM) sites
T2m vs LST relationship varies with many factors:
Windspeed (b, d)
Cloud cover (c, d, e)
Weather systems (f)
Vegetation (also vegetation health and density)
Snow cover
Surface roughness

## Slide 24: T2m vs LST (2)
Max Temperatures
Min Temperatures
Good, E. J. (2016), An in situ-based analysis of the relationship between land surface “skin” and screen-level air temperatures, J. Geophys. Res. Atmos., 121, 8801–8819, doi:10.1002/2016JD025318.
Example here is from 2014 Amazonia ARM site
Red line shows LST-T2m
Green is windspeed
Blue is cloud
‘Saw-tooth’ effect could be due to regular mowing of the site:
Mowing increases soil fraction and reduces vegetation => Large LST-T2m difference
Grass grows again over time => LST-T2m converges

## Slide 25: T2m vs LST (3)
ARM Shouxian (HFE) between 11 May 2008 and 29 December 2008
Timing of daily max/min can be different for LST and T2m
Tmin and LSTmin often occur at the same time (just before dawn)
LSTmax occurs near solar noon
Tmax occurs mid pm.
Good, E. J. (2016), An in situ-based analysis of the relationship between land surface “skin” and screen-level air temperatures, J. Geophys. Res. Atmos., 121, 8801–8819, doi:10.1002/2016JD025318.
T2m vs LST (3)

## Slide 26: LST vs T2m Daily Anomalies
Good, E. J., Aldred, F. M., Ghent, D. J., Veal, K. L., & Jimenez, C. (2022). An analysis of the stability and trends in the LST_cci Land Surface Temperature datasets over Europe. Earth and Space Science, 9, e2022EA002317. https://doi.org/10.1029/2022EA002317
LST_cci MODIS/Aqua – night & day 2002-2018
Station Tmin & Tmax
LST_cci Microwave LST – 6am & 6pm
1996-2020
Station Tmin & Tmax
Anomalies are well correlated and often show similar distributions

## Slide 27: Concluding Remarks
LST is not the same as T2m, however the two are usually closely related
  Can be large differences that vary temporally but generally well correlated
  Anomalies seem to be well correlated
When using any satellite data for climate applications, you must bear in mind that the dataset is not perfect and free from problems.
  Consider the uncertainty and quality information provided (+ validation results)
  Non-climatic discontinuities may result from merging different instruments, input data, satellite overpass time, calibration drift, retrieval errors, … Verifying the stability (and accuracy) of your data should always be step 1 if using time series!
  Bear in mind there are gaps in all LST data records which may affect your results. (In LST_cci, work is just starting on calculating coverage uncertainty.)
Please look at the LST_cci webpages for further information
  Product User Guide (PUG) is essential reading – even if you just look at the ‘Quick Start Guide’
  Please contact us on info.lst-cci@acri-st.fr for help with your application!