## Slide 1: In situ temperature data
Robert Dunn (Met Office)

## Slide 2: Outline
Overview of in situ observations
Station networks
Creating Station datasets
Some issues with station datasets

## Slide 3: Overview of In Situ Observations

## Slide 4: Overview of in situ observations
Measurements at surface weather stations
Temperatures (T, Tw) in a Stephenson screen
  PRT thermometers
Other co-located measurements
  Wind speed & direction (anemometers or sonic)
  Rainfall accumulation (tipping bucket gauges)
  Visibility
  Cloud height(s)
Optionally
  Radiation/Sunshine
  Snow depth
  Soil temperature
  Soil moisture
  …
WMO Guide to Instruments and Methods of Observation (incl. Siting Classifications)

## Slide 5: Types of Station Observations
Manual observers
Automatic Weather Stations (AWS)
Message types (METAR, SYNOP, CLIMAT, DAYCLI)
  And formats (text, BUFR)
Quantities
  Subdaily – instantaneous
  Daily/Monthly
    Extremal (Tmax, Tmin) [Time of observation biases]
    Average (Tavg) [Methodological choices]
    Sums (Precip accumulations) [TOO biases]
Maja K Mikkelsen, The Last Observers https://eu.patagonia.com/nl/en/films/the-last-observers/
Notes: METAR: Airport messages, determined by ICAO (intl. civil aviation organisation). Meteorological Terminal Aviation Routine Weather Report or Meteorological Aerodrome Report
SYNOP: Surface synoptic message (FM-12). Subdaily (6h or 1h if AWS)
CLIMAT: Climate message, monthly averages
DAYCLI : Daily CLIMAT
BUFR: Binary Universal Form for the Representation of meteorological data

## Slide 6: Station networks

## Slide 7: Network changes
Station networks are not stable
  Initial increases while stations are established
  Recent decreases as locations are rationalised
    Stations have an operating cost
    Even spacing more useful
      Early networks had clusters close to urban centres
Ongoing work to increase numbers of stations in global archives
  Overall improvement, but means changes in deep past
Indicative numbers of stations used for gridding in the UK SotC 2024 [top] monthly Tmax, Tmin (1884 to 2024), daily Tmax, Tmin (1931–2024) [bottom] monthly rainfall (1836 to 2024), daily rainfall (1891–2024) (UK SotC 2024, Kendon et al. 2025, Fig A2-A3)

## Slide 8
C3S sub daily data

## Slide 9: Creating station datasets

## Slide 10: Data Rescue
Station records not yet digitised (or imaged)
  Hence unavailable to the scientific community
Both steps are currently labour-intensive
  Citizen science (e.g. Zooniverse)
  Promising developments with AI digitisation
(a): Box files of observations of historical daily rainfall data for the UK held by the Met Office library and archive in Exeter (b) an example of contents: daily rainfall observations in inches for Longwood House, Hampshire for each day of the year 1928. (UK SotC 2024 Kendon et al. 2025 Fig A6 )
Archives at NOAA/NCEI, Asheville, NC (Photo: R Dunn)

## Slide 11: Mingling and merging station records
Station records maybe stored under different IDs
  Especially if combining individual sources
  Or different variables
Geopolitical changes cause station IDs to change (e.g. 1988-90)
Adding rescued data records
Need careful hierarchy of sources
  Most reliable given highest priority
Depends on reliable and complete metadata
Can cause inhomogeneities
Different colours denote distinct source decks and their identifiers in these source decks are given in the inline key. Note that source deck lines often overplot one another. Rennie et al. (2014), Thorne et al. (2017).
GHCN method: Menne et al, 2012

## Slide 12: Quality Control
Manual
  Time intensive
  Concerns about reproducibility
Automatic QC
  Never perfect
  Hard to get right for all climates
Types of QC depend on goal
  presentational purposes (“bullseyes”)
  data accuracy
Reason why CLIMAT has been “flagged”
Facility to look at original coded message
Values derived from alternative SYNOP data source
Values are changed or deleted by typing in these boxes
Manual QC of CLIMAT messages - monthly CRUTEM updates

## Slide 13: Quality Control
Repeated strings
Preferential values
Spikes
Secondary populations
Logic checks
Cross-variable sanity checks
Buddy checks
HadISD: Dunn et al, 2012, Dunn et al, 2016; GHCNd: Durre et al, 2010; C3S: LUG

## Slide 14: Some issues with station datasets

## Slide 15: Station Network & Data Sharing
Open [long term] records heavily skewed to Global North
WMO Unified Data Policy
  Some data shall [must] be shared
  Some data should [maybe] be shared
National networks often much denser than those shared internationally
  “GTS”
  WMO InteGrated Observing System (WIGOS)
  WMO Information System (WIS)
Climate indices have been used to work around sharing restrictions
C3S daily data
~177,000 stations
1763-2026
150 individual sources

## Slide 16: Observation & Human Issues
724797-99999, Milford, UT, USA, 1982
161460-99999, Punta Marina, Italy, 2006
476960-43323, Yokosuka, Japan, 1973
702220-99999, Toronto City, Canada, 1976
Temperature
Temperature
Wind
speed
Dewpoint
Temperature
Examples from HadISD: Dunn et al, 2012 (prior to QC!)

## Slide 17: Other stability issues
Enclosure changes
  Early data used different instruments
  Different enclosures
  Limited metadata
  Modern parallel measurements help
Instrumentation changes
  Hg-in-glass to Pt-resistance thermometers
  Wet-bulb thermometers to capacitor rh sensors
Urbanisation
  And subsequent station relocations
Extreme weather
Mean winter minimum
Lowest temperature of year
Perth (WA)
Site moved in 1992-93 from inner city to park north of city centre (earlier moves 1963, 1967). Post-1993 site about 2C cooler than 1967-92 site for means, 3C cooler for extremes. 1910-1992 record low (1.2C) surpassed 38 times in 21 years since 1994 [Blair Trewin, BOM]

## Slide 18: Homogeneity & Homogenisation
Issues with station merges
  E.g. re-used station IDs
Undocumented station moves
Use comparison with neighbours to identify breakpoints
  Can potentially adjust (monthly, maybe daily data)
Needs to be automatic for large networks
  Can be manual for small networks or national studies
Homogenisation of temperature series in Berkeley Earth dataset
Menne & Williams, 2009

## Slide 19: Marine
The stations move!
Storage media have been shuffled!

## Slide 20: Summary
A short and high-level overview of station observations
Station networks and message types
Issues with data, and routes for quality control
Creation of station-based datasets & and some considerations
Examples of in situ datasets on next slide

## Slide 21: Some in situ datasets
Name | Domain | Type | Timescale | Variables | URL
GHCN(m/d/h) | Global | S | M/D/H | Tg; Tx, Tn; T, Td, Tw; Others | https://www.ncei.noaa.gov/products/land-based-station
C3S | Global | S | M/D/H | T, Td; Others | https://cds.climate.copernicus.eu/datasets/insitu-observations-surface-land
E-OBS | Europe | S, G | D | Tx, Tn, Tg; Others | https://surfobs.climate.copernicus.eu/dataaccess/access_eobs.php & www.ecad.eu/
ECAD | Europe | G | Y/M | T&P indices | www.ecad.eu/
GPCC | Global | G | M/D | P | https://www.dwd.de/EN/ourservices/gpcc/gpcc.html
MIDAS | UK | S | D (H) | Tx, Tn; Others | https://catalogue.ceda.ac.uk/uuid/dbd451271eb04662beade68da43546e1/
BAMS State of the Climate contains lists of datasets used from many sections