## Slide 1
LSTM
Mike Perry
University of Leicester (NCEO

## Slide 2: Land Surface Temperature Mission (LSTM)
“To complement Sentinel observation capabilities with high spatio-temporal resolution Thermal Infra-Red observations over land and coastal regions in support of agriculture management services, and possibly a range of additional applications and services”
LSTM Main Mission Objective

## Slide 3: Land Surface Temperature Mission (LSTM)
Primary objective: to enable monitoring evapotranspiration (ET) rate at European field scale by capturing the variability of Land Surface Temperature (LST) (and hence ET) allowing more robust estimates of field-scale water productivity.
LST goal: accuracy 1.0 K at 300 K
LST & LSE threshold: LST accuracy 1.5 K at 300 K, LSE accuracy 2%
ET goal: accuracy 15% [mm/day], precision 5%, field scale MFU [0.5 ha], daily
ET threshold: accuracy 20% [mm/day], precision 10%, field scale MFU [1 ha], 3 days
Complementary objectives: to support a range of additional services benefitting from TIR observations – in particular:
soil composition
urban heat islands
coastal zone management
High‐Temperature Events.

## Slide 4: Land Surface Temperature Mission (LSTM)
Key requirement | Design Concept
Geometrical revisit | 1 day/4 sats (2d/2s)
Local time | 13:00 (Europe) & night observations
SSD | 50 m (37m at nadir)
Spectral Bands | 5 TIR, 4 VNIR, 2 SWIR
Swath | 700 km, at 640 km altitude
Acquisition system | Whiskbroom scanner
Geo-location L1c | 1 SSD
MTF | 0.2-0.3
Data latency (L2) | 6-12 hours
NeDT | < 0.1 K
ARA | < 0.5 K
Satellite mass | about 1.1 ton

## Slide 5: Land Surface Temperature Mission (LSTM) L2 Study
  Algorithms selection and improvement all along the project :
    Phase 1 : LST, LSE, aerosols, TCWV
    Phase 2 : algorithms evolutions, correction of directional effects + product validation with EVT
  Development of a prototype and an operational processor
  Cal/Val activities (before launch, IOT, routine operations) and performances assessment of L2A products.
  In collaboration with CEM-PAL : support the engagement of a community of users and facilitate their use of LSTM products

## Slide 6: Land Surface Temperature Mission (LSTM) L2 Study
(Science Lead)

## Slide 7: Land Surface Temperature Mission (LSTM) L2 Study
LSTM L2 – LST / LSE Algorithm

## Slide 8: Land Surface Temperature Mission (LSTM) L2 Study
LSTM L2 – LST / LSE Algorithm

## Slide 9: Land Surface Temperature Mission (LSTM) L2 Study
LSTM L2 – LST / LSE Algorithm
 | σLST |  |  |  |  |  | σTCWV
σLST | 1 |  |  |  |  |  | 
 |  | 1 |  |  |  |  | 
 |  |  | 1 |  |  |  | 
 |  |  |  | 1 |  |  | 
 |  |  |  |  | 1 |  | 
 |  |  |  |  |  | 1 | 
σTCWV |  |  |  |  |  |  | 1
 | σLST |  |  |  |  |  | σTCWV
σLST | 1 |  |  |  |  |  | 
 |  | 1 |  |  |  |  | 
 |  |  | 1 |  |  |  | 
 |  |  |  | 1 |  |  | 
 |  |  |  |  | 1 |  | 
 |  |  |  |  |  | 1 | 
σTCWV |  |  |  |  |  |  | 1

## Slide 10: Land Surface Temperature Mission (LSTM) L2 Study
LSTM L2 – LST / LSE Algorithm

## Slide 11: Land Surface Temperature Mission (LSTM) L2 Study
LSTM L2 – Other activities
Algorithm round robin (algorithm selection)

## Slide 12: Land Surface Temperature Mission (LSTM) L2 Study
LSTM L2 – Other activities
Algorithm round robin (algorithm selection)
Calibration and validation
  Campaign data

## Slide 13: Land Surface Temperature Mission (LSTM) L2 Study
LSTM L2 – Other activities
Algorithm round robin (algorithm selection)
Calibration and validation
  Campaign data
  DART simulations