## Slide 1: Session 8: LST Applications 4
Chair: Abigail Waring (University of Leicester)
Notes: Good Morning
I’m Karen Veal from the Surface Temperature Group at University of Leicester. I shall be talking about work done by Darren Ghent, Mike Perry and myself.

## Slide 2
LST_cci Workshop:
Thursday Morning Session
Lizzie Good
(Met Office)

## Slide 3: Thursday Morning Sessions
Conference rooms will be separated
Conf 1 = Plenary & ESMValTool
Conf 2 = LST_cci drop in session (from 10:35)
If you not registered for the ESMValTool training but want to register, please ask.
“LST_cci Workshop: Thursday am & ESMValTool training”

## Slide 4: LST_cci Drop-In Session (Conference Room 2)
Run by the LST_cci project team (Tuesday presenters)
Technical support with using LST_cci including the Regridding & Sub-setting Tool (presentation later today)
Advice on how to use LST_cci data in your application.

## Slide 5: Operational Heat-Risk Monitoring for Solar Farms Using EO-Derived Land Surface Temperature Under High Irradiance Thresholds
Enes Hisam – GMV NSL
Dhritiraj Sengupta – GMV NSL
LST_cci
Workshop
13th May 2026

## Slide 6: EO Best Practices (EOPB) for Solar Energy PROJECT
The EOBP for Solar Energy project is funded by ESA as a series of EO Best Practices.
The project defines best practices for the solar energy users to integrate impactful EO products into their business processes.
Produce EO Best
Practice guidelines
Prepare satellite-based tools for industry to test
Engage with Solar Energy industry stakeholders through interviews and/or workshops
Identify Solar Energy
industry needs
Match current Earth Observation capabilities
1
3
2
4

## Slide 7: To meet industry needs, we have developed two demonstrators hosted on the user-friendly ESA APEx platform
The Solar Energy industry requires reliable, location-specific information to support:
Site selection and investment decisions for new solar farms.
Performance assessment and risk management under varying temperature and radiation conditions.
Why Earth Observation?
Long-term, spatially continuous records
Objective, comparable indicators
Integration with non-EO data
Hosted on a single platform as a comprehensive, efficient and user-friendly solution

## Slide 8: The demo products show the potential of integrating space & terrestrial data sources
Solar Site Farm Selection tool
Combines space & terrestrial data & diverse insights to identify at regional level the most suitable locations for solar farm installation
Temperature Analysis for Solar Radiation Thresholds tool
Leverages space data to support monitoring of PV panel performances across different sites in the region of interest

## Slide 9: The demo products show the potential of integrating space & terrestrial data sources

## Slide 10: Temperature Analysis for Solar Radiation Thresholds tool
Hollyhurst Farm in Warwickshire County, England
Temperature Analysis for Solar Radiation Thresholds tool
Leverages space data to support monitoring of PV panel performances across different sites in the region of interest

## Slide 11: The Temperature Analysis tool leverages spatially consistent space data to support monitoring of PV panel performances
This product provides an in-depth analysis of Land Surface Temperature (LST) variations when solar irradiation exceeds specific thresholds.
Excessive heat can negatively affect photovoltaic (PV) panel performance by causing thermal losses, reducing energy yield, and accelerating material degradation. By conducting LST analysis under high solar irradiation conditions, this tool offers insights to optimize solar farm efficiency.
Main applications include:
🌡️☀️Identifying temperature variations during periods of high solar exposure to understand the thermal impacts on PV panel performance
🔥⚡Helping to identify excessive heat conditions that lead to thermal losses and reduced energy yield, allowing for improved energy output through temperature management strategies
💧🌿Implementing solutions like panel cooling, optimized tilting angles, and vegetation management to reduce the adverse effects of high temperatures on PV efficiency
🧠🔧Insights that enable solar farm operators to plan for temperature-related performance improvements, ensuring optimal panel efficiency throughout the year
Threshold 25 °C exceeded
Source: GMV analysis
Land Surface Temperature (°C)
Solar Irradiation > 0 (W/m2)
Time (HH:MM)
Land Surface Temperature (°C) analysis when Solar Irradiation > 50 (W/m2) (2024-01-04)
Illustrative
As the temperature of a PV panel increases above 25°C, its efficiency tends to decrease

## Slide 12: The demonstration aims at proving that EO can help maximising farm efficiency over a specific period
Parameter | Dataset name | Source | Data type | Spatial resolution | Temporal frequency | Latency | Archive length | Spatial coverage | Access
Solar Irradiation | Surface Solar Radiation Data Set - Heliosat (SARAH) | EUMETSAT | Raster | 0.05° | 30 min | Near Real Time | 1983-Now | Africa-Europe | Link
Land Surface Temperature | Meteosat Second Generation (MSG) LST All-Sky | EUMETSAT | Raster | 0.05° | 30 min | Near Real Time | 1950-Now | Africa-Europe-South America | Link
A new solar farm is planned for development at Hollyhurst Farm in Warwickshire County, England. An LST analysis, with the goal of proving how EO data can help to maximise its efficiency, has been conducted for the entire year of 2024. The analysis identified when solar irradiation exceeds a specific threshold.
Source: GMV analysis
Datasets

## Slide 13: List of product outputs
CSV files for each month in 2024 showing LST and corresponding SIS/DNI data for every 30 min.
Daily Figures shows correlation between LST and SIS/DNI when solar irradiation is above the threshold.
Monthly reports show days when solar irradiation exceeds the threshold.
CSV file shows max/min LST for each day in 2024.

## Slide 14: The tools enables the user to predict peaks in LST, maximizing efficiency of the plant and reducing risks of long-term damages
Accuracy of solar irradiation data: 5 W/m2
Accuracy of LST data: 3 °C
Illustrative
30 min LST analysis when Solar Irradiation exceeds 50 Watt/M²
CSVs

## Slide 15: The tools enables the user to predict peaks in LST, maximizing efficiency of the plant and reducing risks of long-term damages
Accuracy of solar irradiation data: 5 W/m2
Accuracy of LST data: 3 °C
Illustrative
30 min LST analysis when Solar Irradiation exceeds 50 Watt/M²
CSVs

## Slide 16: Example of Max/Min LST with their corresponding time over the targeting solar farm.
Date | Max LST | Time of Max LST | Min LST | Time of Min LST
1/1/2024 | 9.95 | 11:30:00 | 1.96 | 08:30:00
1/2/2024 | 12.08 | 15:00:00 | 11.18 | 10:00:00
1/3/2024 | 12.34 | 11:30:00 | 6.12 | 09:00:00
1/4/2024 | 11.13 | 12:00:00 | 3.72 | 09:00:00

## Slide 17: The tool can be scaled up to monitor multiple farms within the same region based on data from the same source
Source: GMV analysis
LST on 02-06-2024 at specific 30 min interval over the UK (°C)
Solar Irradiation on 02-06-2024 at specific 30 min interval over the UK (W/m2)
08:00
11:30
16:00
Space data tracking solar irradiation and land surface temperature is spatially consistent, achieves high temporal resolution and guarantees availability of historical data.
The same space data from the same sources can be used for multiple farms across the entire monitored region, eventually allowing to build a centralized and uniform monitoring system.
Illustrative

## Slide 18: Key Added Value
High-Temporal Resolution Temperature Mapping: Frequent 30-minute analysis helps detect short-term temperature spikes, enabling timely interventions to reduce the thermal impacts on PV efficiency
Comprehensive Thermal & Energy Mapping: Combining LST with solar irradiation data allows for a holistic understanding of how thermal variations and solar exposure affect photovoltaic (PV) panels
Autonomous Operation: This satellite-based solution functions independently, removing the need for manual temperature measurements or on-site data collection.
Scalable Monitoring: Designed for large-scale operations, the system can monitor multiple solar farms simultaneously across extensive geographic regions. As new satellite data becomes available, it dynamically updates temperature maps to reflect the latest conditions.
Unified Platform for Multi-Site Management: Enables operators to oversee and optimize the performance of an entire network of solar farms from a single, integrated platform. This centralization simplifies operations and maximizes efficiency across all monitored locations
⏱️
🌡️
🤖
📈
🌍

## Slide 19: Looking Ahead: Future Prospects
Customizable Parameters
Allow users to configure solar irradiation thresholds.
Near Real-Time Operation
Transitioning to an operational system that delivers frequent, near real-time temperature updates to enable immediate decision-making.
Multi-Site Solar Farm Management
Scalable architecture designed to monitor and analyze temperature conditions across multiple solar farms simultaneously.
Ground-Truth Validation & Enhancement
Integrating ground-based temperature and performance sensors to validate satellite data and enhance it using AI models.
AI-Driven Pattern Detection
Utilizing machine learning to identify recurring thermal stress patterns, seasonal trends, and long-term heat-related degradation risks.
API & Dashboard Integration
Providing output access through user-friendly dashboards and APIs for easy integration into existing energy management platforms.
🔧
📡
🌍
🧠
📤
📊

## Slide 20: Stakeholder Feedback and Lesson Learnt

## Slide 21: Gathering Feedback
Feedback on the platform were collected in two stages:
Before and during the development which included one-to-one meetings, workshop, and online questionnaire
After the development through online one-to-one meetings with targeted solar energy stakeholders
Sample questions included:
“How well does the current platform reflect the real-world constraints, priorities, and decision processes you face in planning and operating solar projects?”
“In what ways could the platform’s data, functionalities, or visualisations be improved to better support your organisation’s strategic, technical, or financial decision-making?”
“What additional features, datasets, or forms of guidance would make you more confident in using this platform as part of your standard workflow?”

## Slide 22: We have categorized the stakeholder feedback of the demonstrators into nine thematic areas…
Source: GMV analysis.
Feedback
overview
EO operational monitoring & commercialisation
a) Financial and carbon market credibility
a) Scale-sensitive weighting
b) Land surface temperature vs
air temperature
c) Hybrid data approach
Solar irradiation and climate suitability
Grid interconnection & infrastructure accessibility
a) Grid capacity as a limiting factor
b) Road and power station accessibility
a) European coverage and scalability
b) Educational and commercial utility
c) Data harmonization challenges
d) Limited land availability in Europe
Geographical coverage & scalability
Environmental & biodiversity integrity
a) High-resolution biodiversity layers
b) Configurable buffer zones
c) Alignment with global conservation targets
a) Commercial dataset benchmarking
b) Dynamic and up-to-date layers
c) Interoperability and open standards
Data quality, resolution & integration
a) Layered interface design
b) Geospatial reasoning tools
c) Dedicated partnership roles
d) Training and support materials
Context-specific suitability & stakeholder engagement
Usability, customization & capacity building
a) Building connected data ecosystems
b) Integration with solar programmes
c) Credibility through trusted partnerships
d) Bridging the communication gap
Transparency, credibility, and institutional support
a) Intermediate layers for transparency
b) Institutional leadership and outreach
c) Local customization and visibility
d) Strengthens developers’ position with banks and insurers

## Slide 23: …and consolidated it into main findings to inform the EO adoption barriers of the overall EOBP for Solar Energy project
Ground truth validation
EO insights depend on in-situ validation for clear cost-accuracy trade-offs
Build for scale
Move beyond “pilot trap” where good pilots never reach operational scale
New EO adoption barriers identified
Accessibility & usability
End-users need plug & play GUIs, dynamic AOI tools, & cloud processing
Models instead of pixels
AI & ML models will improve insight generation more than higher resolution
Previous EO adoption barrier confirmed
Systematic ground validation required for trust in EO data
Clear methodology needed due to sometimes limited EO/GIS skills
Transparency on limitations for realistic cost-accuracy trade-offs
Validation & confidence
Stakeholders strongly advocated expanding platform coverage
This wider coverage would greatly increase its relevance for developers working across borders
Scalability
Incorporate auxiliary data (e.g. census data, business layers, prohibited areas)
Tailor these datasets to each use case, sourced from relevant local stakeholders
Auxiliary data
Geospatial Explorer praised by solar stakeholders for user-friendliness compared to previous experiences with EO
However, further developments needed to simplify terminology, or show both high-level categories & raw values
Platform accessibility
Scalable AI models designed to monitor and analyse temperature conditions across multiple solar farms simultaneously
Utilizing machine learning to identify recurring thermal stress patterns, seasonal trends, and long-term heat-related degradation risks
Multi solar farm oversight
Consolidated findings
Non-EO data fusion
EO needs to be fused with socio-economic or regulatory data to deliver real value

## Slide 24
Enes Hisam
enes.hisam@gmv.com

## Slide 25
Resolving Angular Inconsistency in GEO and LEO CCI Land Surface Temperature Products Using a Physics-Informed Deep Learning Model
Qiang Na, Sofia L. Ermida, Biao Cao, Isabel F. Trigo, Qinhuo Liu
    Aerospace Information Research Institute,
    Chinese Academy of Sciences,
    Instituto Português do Mar e da Atmosfera,
    Beijing Normal University
Remote

## Slide 26: Land Surface Temperature from OroraTech’s Thermal Infrared Constellation
LST_cci Workshop 2026
Session 8: LST Applications 4
Anastasia Sarelli, Josephine Wong, Christian Mollière, Anna Brand, Andrea Spichtinger, Julia Gottfriedsen

## Slide 27: Hi, we are OroraTech
Visualization,
API
Patented thermal camera
On-Board Processing
Unique constellation for real-time data
170+
Employees on
5
continents
2018
Founded in Munich
35+
Satellite sources
18
Own payloads
in orbit
800+
Users in
25
countries

## Slide 28: Mission
Towards 30 minutes revisit in the thermal infrared
Initial Service
80+ OT satellites
Up to 48 scans
Live monitoring
Since 2020
Today
From 2027
Public Satellites
20-25 scans per day
18 OT payloads in orbit
Up to 4 daily scans closing the afternoon gap
Constellation Build-Up
Full Operational Service

## Slide 29: Constellation update: 4 satellites launched on May 3rd!
Mission patch

## Slide 30: Seeing what others miss: satellites in new orbits
OroraTech satellites are closing the data gap

## Slide 31: Mission characteristics
 | FOREST-2 | OTC-P1
Number of satellites | 1 | 8
Status | Launched | Launched
Orbit | 525 km, Sun-Synchronous Local Time at Descending Node (LTDN) at 13:30 | 525x550km, Sun-synchronous Mean Local Time at Ascending Node (MLTAN) at 16:00+-15 min
Inclination | 97.7° | 97.53°
Acquisition modes | Tasking | Tasking, Monitoring
Revisit time (average) | 7 days | 0.5 days
Imager Type | SAFIRE | 

## Slide 32: Specifications of Instrument
OroraTech Thermal Infrared Camera
Instrument name | SAFIRE
Spectral bands | M0: 3.4 – 4.2 µm
 | L2: 10.4 – 12.5 µm
Product resolution | 200 m
Swath | Design: 410 km Threshold (min.): 330 km
Dynamic range | MWIR: 300 - 650 K
 | LWIR: 260 - 640 K
Viewing angle | 40°
Technology | Uncooled microbolometer detector, no internal blackbody

## Slide 33: Band Specifications
Wildfire Detection & FRP
Land Surface Temperature
Safire-2

## Slide 34: OroraTech Data Products
Overview
WFS & API Tasking, Dissemination, Analysis
Tasking
On-Demand L1+L2
OT Aggregated Active Fire
Wildfire Detection and Monitoring
OT Fire Spread Fire Spread Prediction
OT Burnt Area Burnt Area Mapping
Scan Systematic L1+L2
OT LST Land Surface Temperature
OT NRT Active Fire Near Real Time Fire Detection
OT FireSight AI Short Term Fire Hazard Prediction
Beta
2026
Live
Live
OT SST Sea Surface Temperature
Preview
OT FRP Fire Radiative Power
Live
TOA BT Top Of Atmosphere Brightness Temperature
FOREST Clean Data
Smart Data & Analytics
Level 1
Level 3 & Level 4
Level 2
Preview
Preview
Live
Live
Live
Live

## Slide 35: OroraTech Data Products
Overview
WFS & API Tasking, Dissemination, Analysis
Tasking
On-Demand L1+L2
OT Aggregated Active Fire
Wildfire Detection and Monitoring
OT Fire Spread Fire Spread Prediction
OT Burnt Area Burnt Area Mapping
Scan Systematic L1+L2
OT LST Land Surface Temperature
OT NRT Active Fire Near Real Time Fire Detection
OT FireSight AI Short Term Fire Hazard Prediction
Beta
2026
Live
Live
OT SST Sea Surface Temperature
Preview
OT FRP Fire Radiative Power
Live
TOA BT Top Of Atmosphere Brightness Temperature
FOREST Clean Data
Smart Data & Analytics
Level 1
Level 3 & Level 4
Level 2
Preview
Preview
Live
Live
Live
Live

## Slide 36: Level 2 Land Surface Temperature
Research & Development ongoing
* further improvements expected
GSD | 200 m | 
Swath | 200 km | 
Format | GeoTiff (EPSG:4326) NetCDF (unprojected) | 
Geolocation Accuracy (CE90) | <400m <650m (open ocean) | 
Temperature Accuracy | 3K | 
Latency | Currently 7 days | 
Revisit | 12h (on average at equator) | 
Additional datasets | Cloud mask Image footprint (GeoJSON) | 
Delivery method | Via STAC | 
16°C
Southern France, June 10th 2025
FOREST-2 LST
35°C

## Slide 37: Level-2 LST retrieval
Single-band retrieval using the radiative transfer equation
Level-2
Level-1
Atmospheric modelling and correction
Top of Atmosphere Radiance
LWIR2 band
Image source: Wikipedia
Land Surface Temperature
LibRadTran, upwelling & downwelling radiances
Emissivity estimation and correction
Land cover, NDVI

## Slide 38: Level-2 LST validation
Against ground stations
Ground station networks:
SURFRAD - NOAA Global Monitoring Division
Land Surface Temperature, Aerosol Optical Depth, and Water Vapour Sentinel-3 Products (LAW)
U.S. Climate Reference Network (USCRN)

## Slide 39: Level-2 LST performance
Data Quality evaluated by ESA's Mission Performance Cluster, statement 01/2026
“The comparison between the satellite-derived LST and the in-situ measurements showed a good agreement across the analysed matchups for both (FOREST-2) imagers. Without this cold outlier, these results are in line with the performance objective of the OroraTech LST product, which aims at achieving accuracy better than 3K “
F002/XE007829
F002/XE008208
Further improvements in 2026 expected
→ Target accuracy: <3K

## Slide 40: FOREST-2 LST use cases
Cold
Warm
Forestry and urban dynamics
Los Angeles
January 9th 2025, 01:00 am
Level-2 Land Surface Temperature
FOREST-2 / XE007829
Fire fronts
13.3°C
10.7°C
Los Angeles
Burnt scar

## Slide 41: FOREST-2 LST use cases
Cold
Warm
Urban heat
10.9°C
Central Park
15.5°C
Manhattan
New York
May 11th 2025, 01:36 am
Level-2 Land Surface Temperature
FOREST-2 / XE007829

## Slide 42: FOREST-2 LST use cases
July 11th 2025
June 10th 2025
Before
During HW
Daytime
Marseille
Lyon
Montpellier
Marseille
Montpellier
Lyon
2025 heatwave in South of France
Cold
Warm

## Slide 43: FOREST-2 LST use cases
June 13th 2025
June 27th 2025
Before
Nighttime
During HW
Marseille
Marseille
2025 heatwave in South of France
Cold
Warm

## Slide 44: OroraTech as Emerging Data Provider
ESA Copernicus Contributing Missions Program

## Slide 45: Get free access to OroraTech LST data
Submit your Project Proposal to ESA Third Party Missions program
Each LST data product package contains:
  Image File - GeoTIFF
  Metadata File and footprint - GeoJSON
  Cloud mask - GeoTIFF
Archive products are available starting from 2025
Scan to open the ESA page!
Open to users in ESA member states, ESA Cooperating/Associate States and Canada
Deadline: 30 June 2026

## Slide 46: Thank you!
Anastasia Sarelli
Senior Data Scientist, LST
anastasia.sarelli@ororatech.com
DLR LOT-OT, for German researchers
ESA Third Party Missions,
for researchers in ESA member states and Canada
Or contact us directly!
How to find our data:

## Slide 47
LSTM
Mike Perry
University of Leicester (NCEO
Remote

## Slide 48
End of Day 2
17:00-18:00 - Poster Viewing, Drinks & Canapés
18:00-20:00 – Workshop Dinner
Tomorrow registration between 08:30-09:00